## Slide 1: Organize vSwitch Performance Test Framework
Aihua Li
Huawei Technologies, Inc
12-2014

## Slide 2: Contents
Dissect virtual switch
  End point, switching paths, vLOOP functions
High level repository structure
Test cases and data output
  Throughput: Gbps
  Speed: Mpps
  Latency: usec
  Efficiency: clocks/packets
Desired Test bed configuration.
Test case: PVVP

## Slide 3
Host (Hypervisior)
vSwitch
PHY
port
port
VM1
west
east
port
port
PHY
VM2
west
east
port
port
vLOOP
vLOOP
Tap
vHost
virtIO
TCPIP
vSwitch (Wider Definition)
p2p
v2p
v2v
p2v
One typical brick stack for virtual interface
v
p
p
v
v
v
v
End-point
narrow vswitch definition
tx to PHY != rx by vswitch
Test cases
What tester measures externally
Legend:

## Slide 4: Dissect virtual Switch
Purpose of Virtual Switch
  Moving data from point to point
Where are the end points?
  Narrow definition
    vSwitch port
  Wider definition, from OPNFV’s point of view
    Point is VNF terminals
What are under test?
  P2P, V2V, P2V, V2P ( assume asymmetric )
What are not under test?
  VNF, external wiring.

## Slide 5: Introduce a new VNF service : vLOOP
To compare different vSwitch solutions, need to use same set of VNFs.
  It is desirable for the VNF to be simple, with minimum processing and latency.
vLOOP service
  Simply swap packets between two VNF interfaces
  Sole purpose is for vSwitch testing

## Slide 6: Re-examine end points
End points:
  P: PHY interface
  V: VNF interface ( Note VNF != VM )
  V is totally different than P:
    Big stacks of bricks exist from vswitch port to VNF
    Consume time – part of the switching to be measured.

## Slide 7: Test framework structure
Systems:
  Fedora: build_base_machine
  Ubuntu: build_base_machine
VNFs: note VM images are not to be checked into repo
  vLOOP-dpdk
  vLOOP-virtio
src: directory to manage upstream packages
  Ovs, dpdk, netmap,
Vswitches:
  Ovs-dpdk: setup
  Ovs-kernel: setup
tools:
  Pkt-gen
  Data-collector
Test cases: generic test cases
  P2P, P2P, PVVP, P2V, V2P
Jobs:
  Dpdk.conf
  My.conf
Note the detailed structure would be subject to change based on development. For latest information, refer to the actual git repository.

## Slide 8: System folder
Abstract out details on linux distro:
  Ubuntu: apt-get
  Fedora: rpm
Required Interfaces:
  Build_base_machine
    This script would manually be run once and only once by human tester after the system is freshly installed.
    Collect all required tools
      Gcc, autoconf, make, glibc, …
    Collect required upstream repo for individual vswitches
      Wget ovs-2.3, dpdk-1.6.0r0

## Slide 9: VNF folder
This folder contains different VM images, each contains a flavor of VNF, e.g. vLOOP-dpdk.
The images could be pre-built, or could be made fresh each time the test is run.
For pre-built image, it is best to make a copy of the fresh image as work image, preserve the fresh image intact, and run on the work image, to guarantee test repeatibility
Example:
  vLOOP-dpdk: contains prebuilt VM using testpmd as the vLOOP services.
  vLOOP-virtio: contains a prebuilt VM using linux bridge to connect two virtio interfaces.

## Slide 10: tools folder
Pktgen:
  Dpdk-gen: dpdk packet generator
  Pktgen: netmap packet generator
  Pkt-counter: kernel based packet generator
Data-collector
  Pm-collector: collects data in physical host
  Vm-collector: collects data in VM
VM-Manager
  VM-Start
  VM-Stop

## Slide 11: Vswitch folder
Required interface:
  Setup:
    Compile and build system
    Add-switch
    Add-port
    Add-flow
Ovs-dpdk
  Implementation of API scripts for ovs-dpdk
Ovs-kernel
  Implementation of API scripts for ovs-kernel

## Slide 12: Test cases folder
P2P: Test from PHY->PHY.
PVP: Test from PHY->VNF->PHY.
  Includes VNF speed, vLOOP is prefered
  Does not measure V2V
  Need to include VNF used
PVVP:
  Similar to PVP, but includes V2V path
P2V: Test from PHY->VNF.
  Need to probe VNF
V2P: Test from VNF->PHY.
  Need to tx from VNF
V2V: Test from VNF->VNF.
  Need tx and probe on VNF
PVVP-Overlay:
  Similar to PVVP, with the two VM on separate Host ( See next page )

## Slide 13
Host (Hypervisior)
vSwitch
Host (Hypervisior)
vSwitch
PHY
port
port
VM1
west
east
port
port
PHY
VM2
west
east
port
port
vLOOP
vLOOP
Tap
vHost
virtIO
TCPIP
p2p
v2p
v2v
p2v
v
p
p
v
v
v
v
End-point
Underlay

## Slide 14: Jobs Folder
Contains frequently used job confiugration
  Dpdk.conf
  My.conf
Sample Configuration, dpdk.conf:
    VNF: dpdk-testpmd
    VSWITCH: ovs-dpdk
    # Job listing
    P2P = Yes
    P2V = Yes
    Dpdk-pktgen=yes
    Iperf=yes
    Netperf=yes
To run the sample test:
  Runtest < dpdk.cnf > dpdk.report

## Slide 15: Tests and output data
For each test cases:
  Raw packet tests: dpdk-gen, pkt-gen, pkt-counter
  Iperf
  Netperf
Data to collect:
  Throughput: Gbps
  Packet switching speed: Mpps
  Delay: usec
  Efficiency: clocks/packet

## Slide 16: CPU usage and Efficiency
Efficiency: CPU clocks/packet
  Not direct measurable
  Total GHz = Running GHz * CPU usage
    E.g, for 3 GHz CPU running at 200%, measured 10 Mpps
    Total GHz = 3 GHz * 2 = 6 GHz
    Efficiency = 6 GHz / 10 Mpps = 0.6 GHz/Mpps
  Efficiency convert to clocks/packet
    Hz/pps = (clocks/sec) / ( packet/sec ) = clocks/packet
    0.6 GHz/Mpps  0.6*10^9/10^6 = 600 clocks/packet

## Slide 17: Test bed Examples: PVVP
Host
Host (Hypervisior)
vSwitch
PHY
1
2
VM1
west
east
3
6
PHY
VM2
west
east
4
5
vLOOP
vLOOP
v2p
v2v
p2v
v
p
p
v
v
v
Source Host
Sink Host
Controller Host

## Slide 18: Test Case: PVVP
Hosts list:
  DUT host
  Source host
  Sink host: may share with source host with netname space
  Controller host: share with source or sink host
    All tests are run from controller host
Prepare the test setup:
  Add a switch with 6 ports as shown
  Start two VM instances with vLOOP, connect the interface to vswitch ports appropriately
  Add chaining flows as:
    1->2, 3->4, 5->6
    6->5, 4->3, 2->1

## Slide 19: Test Case: PVVP
Raw packet test:
  Start pktgen from source host
  Start pktgen receive from sink host, collect throughput and Mpps
  Measure CPU usage on DUT host
Iperf test:
  Start iperf server on sink host
  Start iperf session on source host
  Measure CPU usage on DUT
  Collect throughput and Mpps
Netperf test: Similar to iperf test